South of England Hedge Laying Society.

Site Risk Assessment.

| Date: | Task: Hedge Laying | Grid Ref: |
| --- | --- | --- |
| Location: | Nominated Site Foreperson: |

| Hazard | Whom affected | Control Measures(s) | Risk Level |
| --- | --- | --- | --- |
|  |  |  | L | S | R |
| Using a slasher to clear brambles / nettles etc | Hedge layer, Trainers Staff Public | Training / Experience, operate a safe working distance of at least 2 lengths of the slasher handle Do not wear cloves with swinging tools | 1 | 2 | 2 |
| Rabbit holes | Hedge layer, Trainers Staff Public | Training, communication, mark rabbit holes with a stake/ post / hazard tape | 3 | 1 | 3 |
| Removing /& handling barbed wire | Hedge layer, Trainers Staff Public | Training / Experience, use gloves | 1 | 1 | 1 |
| Using Sharp Hand tools, billhooks, axe | Hedge layer, Trainers Staff Public | Training / Experience, keep the public away from hedge laying operators. Cut away from your body, / people, do not wear gloves to hold axes or billhooks | 3 | 2 | 6 |
| Chainsaw operation | Hedge layer, Trainers Staff Public | Full Chainsaw PPE, Operator to hold relevant chainsaw certificate | 3 | 3 | 9 |
| Felling hedge row material | Hedge layer, Trainers Staff Public | Good observations maintained, Training / Experience, safe working distance maintained. Public to be a minimum of 2 shrub / hedgerow plant lengths away, marked by hazard tape | 2 | 1 | 2 |
| Moving long hedge row material / binders and other hitting people | Hedge layer, Trainers Staff Public | Good observations maintained, Training / Experience, safe working / observation distance maintained Public to be a minimum of 2 binder lengths away, marked by hazard tape | 2 | 1 | 2 |
| Lifting heavy items | Hedge layer, Trainers | Training / Experience, Communication, Team work | 1 | 2 | 2 |
| Slip, trip, fall | Hedge layer, Trainers, Public | Remove trip hazards, keep the site tidy, wear boots with good grips. Do not walk about with your hands in your pockets. | 1 | 1 | 1 |

Continued on next page

Site Risk Assessment (continued)

| Nearest Phone: mobile phones on site Pocket | First Aid Box Location: On Hedge line |
| --- | --- |
| Ambulance Meeting Point: | First Aider: Gary Moore Mike Parrott Phil Hart |
| Nearest Hospital/Medical Facilities: | First Aid Contingency: First Aid Kit Small cuts – first aid Medium injuries – non life threatening. First aid then take to hospital if ok to move the patient. Major injuries- life threatening. First aid, then call ambulance. |
| Risk Assessment Undertaken by: P J Hart |
| (L) LIKELIHOOD 1 Hazard exists very infrequently; limited numbers exposed 2 Likely to occur; hazard exists intermittently or occurs occasionally 3 Likely to occur soon; permanent hazard or occurs daily/repeatedly; many may be exposed | (S) SEVERITY OF HAZARD 1 Could cause minor injury only 2 Could cause major injury/3 day or more absence 3 Could cause a fatality/severe injury | (R) RISK LEVEL is the product of Likelihood and Severity (L x S) Very High Risk score 6 or 9 Moderate Risk score 3 or 4 Low Priority Risk score 1 or 2 |

VERY HIGH RISK SCORES (6 TO 9) NEED ADDITIONAL ACTION.  ACTIVITY MUST NOT COMMENCE.

Please turn over & complete the next page

Site Risk Assessment (continued)

Note: If this additional page is needed the results MUST be used when assessing the hazards and risk level of the task

| Hazard | Whom affected | Control Measures(s) | Risk Level |
| --- | --- | --- | --- |
|  |  |  | L | S | R |
| If present Over Head Power lines | Hedge layer, Trainers Staff Public | Get them turned off before laying commences or do not lay the hedge if with in 2 tree lengths of the standing hedge | 3 | 3 | 9 |
| Pricked by Blackthorn | Hedge layer, Trainers Staff Public | Wear gloves when handling blackthorn. | 3 | 1 | 3 |
| Saw dust | Hedge layer, Trainers Staff Public | Wear safety goggles when close to wood being cut | 3 | 1 | 3 |
| Twigs / thorns scratching your eyes | Hedge layer, Trainers Staff Public | Wear safety goggles when close to Twigs / thorns | 3 | 1 | 3 |
| Bruised hands/ fingers/ / legs from Mell / maul / sledge / lump hammer | Hedge layer, | Training / Experience | 2 | 1 | 2 |
| Stabbing feet with a fork | Hedge layer, Trainers | Strong stout boots preferably with steel toecaps | 1 | 1 | 1 |
| Wet ground /ditch slipping | Hedge layer, Trainers, Public | Tread carefully, keep a tidy worksite Appropriate foot ware with good grips | 2 | 1 | 2 |
| Traffic on road | Hedge layer, Trainers, Public | Warning Signs, Good Observations | 2 | 3 | 6 |
| Petrol explosion / flash fire / face scald burns | Chainsaw operators | Caution filling hot chainsaw, let it cool down, use funnel or specialist fuel can nozzle to reduce spillage Start saw 10 m away from the refuelling site. | 2 | 3 | 6 |
| Horses & Riders | Hedge layer, Trainers, Public Horse riders | Good observations & communication. No sudden movements if horses are approaching / passing. Do not start / operate chainsaws if horses are approaching / passing | 2 | 3 | 6 |
| Wasps nest | Hedge layer, Trainers, Public | Mark with a stick, hazard tape, do not lay the cant affected until made safe. | 1 | 3 | 3 |
| Kneeling down, thorn puncture wounds to knees & hands. | Hedge layer, Trainers, | Use knee pads & wear gloves when kneeling & getting up. Alternatively do not kneel & do all the cutting from a standing position. | 1 | 2 | 2 |
| Use of Pruning Saw, (Silky Saw) | Hedge layer, Trainers | Keep spare hand away from the cutting blade. Alternatively wear gloves to help prevent cuts to the back of your fingers / hand | 1 | 2 | 2 |
| Additional Controls Needed: If working near power lines they must be switched off before the job can start. |
| Further Preventative Measures: Chainsaw operators require certification before chainsaw use can take place. Staff and trainers to ensure safe working distances are maintained. |
| Additional Personal Protective Equipment: Chainsaw Operators each to carry their own personal first aid kit at all times. |
| Training Needed: All Novice hedge layers |
| Monitoring and Communication. Training Officer / site foreperson to discuss with the land owner / site manager and update this risk assessment as deemed necessary. Mobile phones on site, check for signal. |

Updated P J Hart March 2017